## Slide 1
Hardware-in-the-loop testing: The difference for de-risking microgrids
Kati Sidwall
Technical Marketing Manager, RTDS Technologies
kati.sidwall@ametek.com

## Slide 2
Why hardware-in-the-loop?!
How do we validate that a system will operate as expected (and to grid code / defined requirements) before commissioning?
How detailed is our system representation when we model and test?
How confident are we that multiple devices in the system are interoperable through a variety of scenarios?
How wide a range of system conditions are we modelling and testing for?
Hardware-in-the-loop reduces risk and improves reliability through highly detailed system modelling and device testing

## Slide 3
Predicting vulnerabilities with EMT simulation
Electromagnetic transient (EMT) simulation captures behaviour associated with inverters that positive-sequence-only study tools may miss
NERC: strong need for EMT modelling in support of renewable energy integration

## Slide 4
Advantages of HIL testing
As close as it gets to field testing but in a safe and highly flexible lab environment (impose a wide range of conditions)
Test multiple controllers simultaneously to see how they interoperate / interact using physical hardware
Reduce risk of control or protection maloperation
NERC 2020 Technical Report detailed the need to identify potential interactions between inverter controls, HVDC, protection, and other grid assets
Testing protection near a wind farm in Texas
Source: Quanta Technology

## Slide 5
Source: ComEd
Commissioned in 2018 | Located at Maywood, Illinois
Major project areas:
HIL testing and validation of emerging technologies such as microgrid controller, DER management system, distribution state estimation
Protection and relay testing
Cybersecurity projects
RTDS is the heart of RT-HIL test setup
Several Microgrid projects in Collaboration with Department of Energy (DOE), National Science Foundation (NSF), Universities, and National Laboratories
ComEd Grid Integration and Technology Lab
RT-HIL Facility

## Slide 6
Secondary microgrid control testing at ComEd
7 MW aggregate load, serving approximately 1,000 residences, businesses and public institutions
Powered by DERs – 750 kW solar PV, 500 kW/2MWh battery storage, 4.8 MW controllable generation
Can cluster with IIT Campus Microgrid – one of the most advanced urban microgrid clusters in the USA
Microgrid master controller for islanding/reconnection, optimization, peak shaving tested with the RTDS Simulator in the ComEd Grid Integration and Technology Lab
Bronzeville Community Microgrid (Chicago)
Source: ComEd

## Slide 7
Source: ComEd
Hardware-in-the-loop setup

## Slide 8
What it looks like in the lab
Source: ComEd

## Slide 9
Results
Source: ComEd
Planned islanding test results shown here
Microgrid stakeholders feel confident in performance through a wide range of conditions
Improves vision of true system dynamics, reducing blindness to vulnerabilities
Source: ComEd

## Slide 10
Thank you!
Questions?
Kati Sidwall
Technical Marketing Manager, RTDS Technologies
kati.sidwall@ametek.com